## Slide 1: Types of Maps
3

## Slide 2: Types of Maps
Topographic Map
  Most widely used
Topography
  Shows natural, constructed features
  Shows elevation

## Slide 6: Topographic Maps
Advantages
  Shows size, shape and elevation
Elevation on Topographic Maps
  Contour Lines
  Reflect shape of land
  Relief – difference in elevation
  Contour Interval
  Index Contours

## Slide 7: Landforms on Topographic Maps:
Widely spaced contour lines = Little change in elevation
Narrowly spaced lines = steep surface

## Slide 8
V-shaped lines = Valleys
Closed loops = Hilltop or depression

## Slide 11: Geologic Maps
Show distribution and types of rocks
Layer one map on top of another
Rock units:
  Geologic Unit
  Color coded and abbreviated letters

## Slide 12: Geologic Maps

## Slide 14: Other Structures
Contact Lines
Strike
Dip

## Slide 16: Soil Maps
Classify, map and describe soils
NRCS
Soil Surveys—3 Parts
  Text-General info.
  Maps-2 types
    General Map
    Detailed Map
  Tables
Uses of Soil Maps—Who uses them?

## Slide 19: Other types
Maps to plot…
  Water
  Air movement
  Temperatures